## Slide 1: Biomedical Monitoring for Astronauts
Team 310 4/4/2024

## Slide 2: Table of Contents
Team Introduction
Project Assignment
  Project Description
  Motivation
  Selected Design
Design Implementation
  System Overview
  Sensor Protocols
  PCB Overview
  Software Overview
Budget & Future Work
Lessons Learned

## Slide 3: Team Introductions
Evan Cloutier
Project Manager
Nick Billmire
Digital Comm. Engineer
Jada Davis
Software Engineer
Landon Hicks
PCB Design Engineer
Austin Roberts
Sensors Engineer
Dallas Toth Test Engineer

## Slide 4: Sponsor and Advisors
Sponsor
L3Harris Technologies
Faculty Advisor
Babak Noroozi, Ph.D.
Professor

## Slide 5: Project Assignment

## Slide 6: Original L3Harris Project Description
Multi-Axial Angular Sensor:​
A form/fit/function replacement​
Design a circuit card assembly for a provided sensor​
Develop code needed to output the proper message format ​
Construct the card within given size limitations​
Regulate power to the sensor​
Output in RS-422 message format

## Slide 7: Current Project Description
Sensor package capable of monitoring an astronaut’s vital signs and spacesuit environment during extravehicular activity (EVA).
Transmit sensor data to the main communications system via a serial interface.
Detect abnormal readings and trigger appropriate alarms.

## Slide 8: Motivation Behind Concept Generation & Selection
Attempts to adapt original project scope
  Limited definition
  Use of IMU's
Decision to explore new, unique project ideas
  Research & Deliberation
  Inspiration from prior research projects
Final Project Definition
  Wearable Sensor Suites
    Work-out sleeve containing IMU’s
    Biomedical monitoring for astronauts (BMA)

## Slide 9: Selected Design
Wearable sock
  Heart rate sensor
  Pulse oximeter
  Thermometer
  Galvanic skin response sensor
Spacesuit environment sensors
  CO2
  Pressure
  Temperature/Humidity
Goal: create a proof-of-concept design to be used for testing and research purposes.
Artistic rendering only; not an actual depiction.
Sensing Sock and Environment Sensor Package

## Slide 10: Design Block Diagram

## Slide 11: Design Implementation

## Slide 12: Sensor System - Overview
BMP280 – Pressure (Pa)
Telaire T6793 – CO2 Concentration (ppm)
MAX30205 – Body Temperature
ECG_GSR Click – GSR Sensor PCB
SHT85 – Ambient Temperature and Humidity
MAX-REFDES117 – Heart Rate and Pulse Oximetry

## Slide 13: Sensor System
Notes: Photo of the breadboard with sensors on it here. Explain the connections without going into detail about software or each sensor’s specs

## Slide 14: Sensor Protocols
Amongst other communication protocols, I2C and SPI interfaces protocols are used in the design.
  I2C was used for the sensor suite.
  SPI for the RFID and SD card applications.
Due to the nature of both protocols, it was within best judgement that these two protocols were the most applicable for this design.

## Slide 15: Radio Frequency ID
Suggested per our advisor to attempt to apply RFID as a means of wireless communication.
Assess whether RFID could be used to transmit data in real time.

## Slide 16: RFID System Overview
Constantly reading and rewriting (no need for WORM)
RF carrier frequency (860 – 960) MHz
Max RF power: 25dBm / 315mW

## Slide 17: System Power
40mA theoretical current draw
7.5V battery pack constructed from AA batteries
50-62.5hr life

## Slide 18: Printed Circuit Board – Overview
2-layer board
  Ground plane
  Power/signal plane
FR-4 substrate
50 x 51.6mm
37 Through vias

## Slide 19: PCB Design
Notes: Include where we will order the PCB from, or if it will be made by Hooker
Mention how many layers the PCB will have, also pricing if available, and justify these.
Consider how to assemble the PCB, especially how to connect middle layers to the pin (not needed for the presentation, but important to think about).

## Slide 20: Software – Overview
Main functions:
Read Sensor Data
Display Sensor Data
Analyze Sensor Data
Store Sensor Data
Hardware Utilized:
STM32F4 Discovery Board MCU
LCD I2C Character Display
Buzzer

## Slide 21: Software Architecture
Display sensor data –> LCD
  Each sensor reading displayed on a timer on a continuous slide.
  Update in real time.
Sensor | Pulse Ox | Heart Rate | GSR | CO2 | Pressure | Temp | Humidity
Unit | SpO2% | Beat/min | Ohms | ppm | atm | Celcius | Relative%

## Slide 22: Software Architecture cont.
Analyze sensor data
  Watch for concerning values
    Thresholding readings
  Display warnings –> LCD
  Trigger alarms -> Buzzer
    Pulse Width Modulation
    Alarm will sound in 3 second intervals
WARNING
CHECK VITALS

## Slide 23: Software Architecture cont.
Store sensor data
  CSV files --> SD Card
  All current sensor data will be written to the file every 10 seconds
Time | Sensor | Reading

## Slide 24: Budget & Future Work

## Slide 25: Budget Breakdown

## Slide 26: Future Work
Formal tests done with PCB
  Sensor readings
  Alarm thresholds
Construct final wearable
  Sensors onto sock
  Housing unit for PCB
Address limitations of pulse ox and heart rate sensor
  Reliability

## Slide 27: Future Work
PCB Housing
Reliability & Redundancy
Systems in place for failures
Power failure backup power
Software in place for malfunctions and inaccurate readings to detect when sensor broken
Managing battery life

## Slide 28: Lessons Learned
Clearly defined and well documented project outline is important.
  Organization ensures efficiency
PCB Design Process
Sensor Integration

## Slide 29: Questions?

## Slide 30: Additional Slides & Resources

## Slide 31: Backup Slides Index
Citations
Full B.O.M.
Details for sensors and their algorithm(s)
MCU Details
RFID Details
I2C vs. SPI Benefits & Drawbacks

## Slide 32: Citations
Fei, D.-Y., Zhao, X., Boanca, C., Hughes, E., Bai, O., Merrell, R., & Rafiq, A. (2010). A biomedical sensor system for real-time monitoring of astronauts’ physiological parameters during extra-vehicular activities. Computers in Biology and Medicine, 40(7), 635–642. https://doi.org/10.1016/j.compbiomed.2010.05.001

## Slide 33: Bill of Materials
 | SD Team 310 - Bill of Materials |  |  |  |  |  |  | 
 | Item Ref # | Description | Part Num. | Quantity | Unit | Unit Cost | Cost | Total Cost
Bio. Sensing | 1 | Sock | N/A | 1 | 6 pack | $15.00 | $15.00 | $15.00
 | 2 | Heart Rate / Blood O2 Sensor | MAXREFDES117 | 2 | individual | $19.02 | $38.04 | $38.04
 | 3 | Body Temperature | MAX30205EVSYS# | 2 | individual | $59.55 | $119.10 | $119.10
 | 4 | Skin Galvanic Sensor | MIKROE-4500 | 2 | individual | $27.00 | $54.00 | $54.00
 | 5 |  |  |  |  |  |  | $0.00
Env. Sensing | 8 | CO2 Sensor | T6793-5K | 2 | individual | $38.90 | $77.80 | $77.80
 | 9 | Pressure Sensor | BMP280 | 2 | individual | $9.95 | $19.90 | $19.90
 | 10 | Humidity Sensor | SHT85 | 2 | individual | $32.18 | $64.36 | $64.36
 | 11 |  |  |  |  |  |  | $0.00
 | 12 |  |  |  |  |  |  | $0.00
Processing | 13 | Microcontroller | STM32F407G-DISC1 | 2 | individual | $21.39 | $42.78 | $42.78
 | 14 | SD Card Storage | SDSDAF3-008G-I | 2 | individual | $11.37 | $22.74 | $22.74
 | 15 | SD Card Holder | 410-123 | 2 | individual | $11.86 | $23.72 | $23.72
 | 20 |  |  |  |  |  |  | $0.00
 | 22 | Character Display | AMC2002CR-B-B6WTDW-I2C | 2 | individual | $16.68 | $33.36 | $33.36
 | 23 | MCU (new & simplified) | NUCLEO-C031C6 | 2 | individual | $10.75 | $21.50 | $21.50
 | 24 | RFID Reader | Yanzeo SR3308 | 1 | individual | $189.00 | $189.00 | $189.00
 | 25 | Mini Micro Jst 2.0 Ph 4 Pin Connectors |  | 1 | pack of 20 | $7.56 | $7.56 | $7.56
 | 26 |  |  |  |  |  |  | 
 | 28 | MPU | MSPM0G3507SPMR | 2 | individual | $2.50 | $5.00 | $5.00
 | 29 | Electrodes for skin |  | 1 | pack of 4 | $8.99 | $8.99 | $8.99
 | 31 |  |  |  |  |  |  | $0.00
 | 32 | RFID CHIP | EM4325V21TP8B+ | 3 | individual | $1.63 | $4.89 | $4.89
 |  |  |  |  | Assuming total shipping cost of 15% |  | $112.16 | $859.90

## Slide 34: Sensor Details
Sensor Reading | Sampling Time | Precision | Reading Range | Reading Format | Typical Reading
GSR | 30 ms | 6-bit | 0-63 | 6-bit digital | ~32
HR & Pulse Ox | 4 seconds | 1 bpm/1% |  | BPM, % | 50-100, >95%
Pressure | ~7 ms | 1 Pa | Up to 110 kPa | Pa | 20-100 kPa
CO2 | 5 seconds | 45 ppm +3% | 0-5000ppm | ppm | < 2000 ppm
Body Temp | 5 ms | 16-bit S (2^-8) | Up to 80C | C | 92-99 F
Temperature | 5 ms | 1 deg F | -40 to 105C | C or F | 60-70 F
Humidity | 5 ms | 1% | 0-100% | % | 20-60%

## Slide 35: Heart Rate & SpO2 Algorithm
Collect sensor data for 4 seconds, sample rate 25 Hz.
Zero-mean: the readings are typically on the order of around 100,000 otherwise. We also re-index the samples to be from –49.5 to +49.5, instead of 0 to 100.
Calculate the signal’s baseline (linear regression). Then subtract this baseline from the signal.
For heart rate: This is done by finding the first local maximum of the IR chan autocorrelation.
For SpO2: compare the relative intensities of R to IR using the RMS level of the zero-mean baselined signal compared to the mean of the raw signal. This quantity is called the Z ratio.
Plug the Z ratio into a corrective formula: SpO2 = (-45.06*Z + 30.354)*Z + 94.845.
Check that the correlation coefficient between R and IR channels greater than certain threshold (say 0.8). If it’s not, then discard the datapoint as erroneous.

## Slide 36: OSHA CO2 Exposure
CO2 Concentration | Exposure Symptoms
5,000 ppm (0.5%) | OSHA limit (8 hours)
10,000 ppm (1.0%) | Possible drowsiness
15,000 ppm (1.5%) | Mild respiratory stimulation
40,000 ppm (4.0%) | Immediately dangerous to life and health

## Slide 37: MCU Details
STM32F407G
Clock rate: up to 168 MHz
ARM Cortex M4, NVIC, MPU, FPU
1 MB flash, 112 KB + 16 KB SRAM
Peripherals: ethernet interface, CRC, USB interfaces, DMA, ADC, DAC, SPI, I2S, I2C, CAN, USART, 9 GPIO ports (16 pins each on most), Watchdog timer, 14 timers
STM32C031C6
Clock rate: up to 48 MHz
ARM Cortex M0
32KB flash, 12KB SRAM
-40C to 85C operating temp
Peripherals: USARTS, SPI, I2C (1 Mbps), DMA, ADC, 45 GPIO, 8 timers

## Slide 38: Typical Spacesuit Conditions
Pressure: ~32.4 kPa (Armstrong's limit is 6.25 kPa)
Air composition: usually pure oxygen, with some water vapor
The sensors already in a space suit can vary, but are not contained in a single small garment.

## Slide 39: RFID Info ref.
4096 bits non-volatile memory (EEPROM)
Forward (Transmission) rates 26.7 -128 kbps
Return rate – 40 to 640 kbps
Erase and write commands
Per manufacturer - applications include sensor monitoring, front end embedded syst, Gen2 communications for wireless data exchange, etc.
Reader range: 25m max

## Slide 40: RFID IC Flowchart

## Slide 41: Protocol Benefits
SPI
Speed
Can send data in real time
Full duplex
Ideal for interfacing to memory
Devices are independently addressable
Low power consumption
Fewer connections
Longer distance compared to SPI
I2C

## Slide 42: Potential Drawbacks
SPI
Requires individual CS (chip select) lines in multiple peripherals
More wire connections
Short distance
Susceptible to noise
I2C
Half-Duplex
Increased processing overhead (more space)
Address conflicts
Susceptible to noise

## Slide 43: Slide Headline
Try to keep text at 16 pt minimum.

## Slide 44: Slide Headline
Try to keep text at 16 pt minimum.
Try to put as few words as possible on the slide if you’re using for a presentation.

## Slide 45: Slide Headline
Try to keep text at 16 pt minimum.
Try to put as few words as possible on the slide if you’re using for a presentation.
Mix and match the backgrounds as shown in this template or just use one throughout.

## Slide 46: Slide Headline
Try to keep text at 16 pt minimum.
Try to put as few words as possible on the slide if you’re using for a presentation.
Mix and match the backgrounds as shown in this template or just use one throughout.
You can put department/unit logos in slide master at Horizontal 0.89” Vertical 6.44” From top left corner

## Slide 47
This is 10-point
This is 15–point Times
This is 20–point
This is 25–point
This is 30–point
This is 35–point
This is 40–point
This is 50–point
This is 60–point
This is 72–point
Notes: Use at least 20-point font in Room A105, B134, and B136
Use at least 25-point font in Room B135

## Slide 48: College of Engineering Color Palette
Fang
Orange
RGB: 238, 118, 36
Hex: #EE7624
CMYK:2, 66, 99, 0
1 2 3 4
1 2 3 4
White
Pantone: PMS 000C
RGB: 255, 255, 255
Hex: #FFFFFF
CMYK: 0, 0, 0, 0
1 2 3 4
Black
Pantone: Black C
RGB: 0, 0, 0
Hex: #000000
CMYK:0, 0, 0, 100
Garnet
Pantone: PMS 195 C
RGB: 120, 47, 64
Hex: #782F40
CMYK:19, 90, 50, 55
1 2 3 4
Notes: Avoid 75% Black in B135

## Slide 49: Accent Color Palette
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
1 2 3 4
Turquoise
RGB: 64, 224, 208
Hex: #40E0D0
CMYK:
1 2 3 4
American Orange
RGB: 255, 139, 0
Hex: #FF8B00
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Asagi-iro
RGB: 72, 146, 155
Hex: #48929b
CMYK:
1 2 3 4
Gainsboro
RGB: 220, 220, 220
Hex: #DCDCDC
CMYK:
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Imperial
RGB: 104, 40, 96
Hex: #682860
CMYK:
1 2 3 4
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Notes: Remove American orange add hyperlink grey
Make corn the last for b135
All work in 134 imperial move later
Tardis doesn’t work in b136

## Slide 50
https://color.adobe.com/create/color-wheel
Analogous
F7AB19
D67F15
EE7624
D64615
F73119
Monochromatic
6E3610
F0A16C
EE7624
6E4931
BASB1C
Triad
A14508
4BED3B
EE7624
250CED
2010A1
Complementary
FF8C40
EE7624
0098A1
24E2ED
A1470C
Split Complementary
28A164
2FED8D
EE7624
0848A1
1871ED
Double Split Complementary
3BED93
EE7624
0C6AED
ED2F18
EDAC2F
Square
C7ED3B
EE7624
0CE1ED
A418ED
ED660C
Compound
87724A
EE7624
60EFCF
09BA61
BA7E09
Shades
6E3610
EE7624
FA7625
D46820
AD551A
Notes: These are the variants that work well with Fang Orange. The bolded items show well on the projectors.

## Slide 51
https://color.adobe.com/create/color-wheel
Analogous
85412D
8F3831
782f40
8F3176
792D85
Monochromatic
C44D69
8E626D
782F40
C48796
451B25
Triad
C43959
78743B
782F40
236178
43A2C4
Complementary
C46078
782F40
25C43D
2F783A
C43959
Split Complementary
93C460
577835
782F40
39C49D
297861
Double Split Complementary
5A783B
782F40
237860
6E2978
784435
Square
78683b
782F40
237830
293978
782337
Compound
DEBAAF
782F40
5D8555
70AB32
AB4D32
Shades
C44D69
782F40
853447
5E2532
38161E

## Slide 52
B135 Stage Right
A105
A105
B135 Stage Left
B135
B134, A105
B136